Transmitter:

;P2PSEND.ASM

list  p=16F84a

__config   h'3ff1'

radix   hex

;-------------

tmrO	equ 0x01

status	equ	0x03

porta	equ	0x05

portb	equ 0x06

intcon	equ	0x0b

sendreg	equ	0x0c

count	equ	0x0d

countaux	equ		0x0e

dataidl	equ 0x0f

optreg	equ	0x81

trisa	equ	0x85

trisb	equ 0x86

;       bit equates

c	equ	0

rpO	equ	5

org 0x000

start

bsf	status , rpO ;bank1

movlw	b'00000000' ;porta output

movwf	trisa

movlw	b'00001111' ;portb first four input

movwf	trisb

movlw	b'0000'

movwf	dataidl

bcf	status, rpO  ;bank0

bsf	porta, 1  ;output mark, bit 1

switch

movlw	h'FF'

movwf	countaux

;--------------

movf	portb, 0 ;w <- portb

movwf	dataidl  ;dataidl <- portb

movlw	b'0000'  ; 0000 <- wreg

subwf	dataidl, 1

btfsc	status, 2  ;idle case

call	serout_idl

;----------------

btfsc	portb , 0

call	serout_fw

btfsc	portb , 1

call	serout_bw

btfsc	portb , 2

call	serout_rt

btfsc	portb , 3

call	serout_lt

goto switch

circle

goto	circle

serout_idl

movlw	b'10000000'

movwf	sendreg

bcf	intcon, 5

bcf	intcon, 7

clrf	tmrO

clrwdt

bsf	status, rpO

movlw	b'11011000'

movwf	optreg

bcf	status, rpO

movlw	h'8'

movwf count

bcf	porta, 1

clrf	tmrO

bcf	intcon, 2

goto time1

serout_fw

movlw	b'11110000'

movwf	sendreg

bcf	intcon, 5

bcf	intcon, 7

clrf	tmrO

clrwdt

bsf	status, rpO

movlw	b'11011000'

movwf	optreg

bcf	status, rpO

movlw	h'8'

movwf count

bcf	porta, 1

clrf	tmrO

bcf	intcon, 2

goto time1

serout_bw

movlw	b'10010000'

movwf	sendreg

bcf	intcon, 5

bcf	intcon, 7

clrf	tmrO

clrwdt

bsf	status, rpO

movlw	b'11011000'

movwf	optreg

bcf	status, rpO

movlw	h'8'

movwf count

bcf	porta, 1

clrf	tmrO

bcf	intcon, 2

goto time1

serout_rt

movlw	b'10110000'

movwf	sendreg

bcf	intcon, 5

bcf	intcon, 7

clrf	tmrO

clrwdt

bsf	status, rpO

movlw	b'11011000'

movwf	optreg

bcf	status, rpO

movlw	h'8'

movwf count

bcf	porta, 1

clrf	tmrO

bcf	intcon, 2

goto time1

serout_lt

movlw	b'11010000'

movwf	sendreg

bcf	intcon, 5

bcf	intcon, 7

clrf	tmrO

clrwdt

bsf	status, rpO

movlw	b'11011000'

movwf	optreg

bcf	status, rpO

movlw	h'8'

movwf count

bcf	porta, 1

clrf	tmrO

bcf	intcon, 2

time1

btfss	intcon, 2

goto	time1

bcf	intcon, 2

nxtbit

rlf	sendreg, f

bcf	porta, 1

btfsc	status , c

bsf	porta, 1

time2

btfss	intcon, 2

goto	time2

bcf	intcon, 2

decfsz	count, f

goto	nxtbit

bsf	porta, 1

time3

btfss	intcon, 2

goto	time3

bcf		intcon, 2

decfsz 	countaux, f

goto	time3

bsf		porta, 1

return

end

Receiver:

list    p=16F84a

__config  h'3ff1'

radix   hex

tmr0	equ	0x01

status	equ	0x03

porta	equ	0x05

portb	equ	0x06

intcon	equ	0x0b

rcvreg	equ	0x0c

count	equ	0x0d

temp	equ	0x0e

datafw	equ 0x0f

databw	equ 0x10

datart	equ 0x11

datalt	equ 0x12

dataidl	equ 0x13

optreg	equ	0x81

trisa	equ	0x85

trisb	equ	0x86

rp0	equ	5

org	0x000

start

bsf		status, rp0

movlw	b'00000101'

movwf	trisa

movlw	b'00000000'

movwf	trisb

bcf		status, rp0

clrf	portb

clrf	rcvreg

switch

btfsc	porta, 2

goto	switch

call	ser_in

movlw	b'11001010'

movwf	dataidl

movlw	b'11011010'

movwf	datafw

movlw	b'11010110'

movwf	databw

movlw	b'11001100'

movwf	datart

movlw	b'11010101'

movwf	datalt

movf	rcvreg, 0 ;w <- rcvreg

subwf	dataidl, 1

btfsc	status, 2  ;idle case

clrf 	portb

subwf	datafw, 1

btfsc	status, 2  ;first comparison

bsf 	portb, 0

subwf	databw, 1

btfsc	status, 2  ;second comparison

bsf 	portb, 1

subwf	datart, 1

btfsc	status, 2  ;third comparison

bsf 	portb, 2

subwf	datalt, 1

btfsc	status, 2  ;fourth comparison

bsf 	portb, 3

goto	switch

ser_in

bcf		intcon, 5

bcf		intcon, 7

clrf	tmr0

clrwdt

bsf		status, rp0

movlw	b'11011000'

movwf	optreg

bcf		status, rp0

movlw	0x08

movwf	count

sbit

btfss	porta, 0

goto	sbit

movlw	0x80

movwf	tmr0

bcf 	intcon, 2

timel

btfss	intcon,2

goto	timel

btfss	porta,0

goto	sbit

clrf	tmr0

bcf		intcon,2

movf	porta,w

movwf	temp

rrf		temp, f

rlf		rcvreg, f

decfsz	count, f

time_aux

btfss	intcon,2

goto	time_aux

btfss	porta,0

goto	sbit

clrf	tmr0

bcf		intcon,2

movf	porta,w

movwf	temp

rrf		temp, f

rlf		rcvreg, f

decfsz	count, f

time2

btfss	intcon,2

goto	time2

bcf		intcon,2

movf	porta,w

movwf	temp

rrf		temp, f

rlf		rcvreg, f

decfsz	count, f

goto	time2

time3

btfss	intcon,2

goto	time3

return

end